## Slide 1: POWER, AIX, HMC …. Les nouveautés 2019
Enterprise Pools 2.0
IBM Power Virtual Servers in IBM Cloud
HMC / CMC
New COD capabilities
Roadmaps
System engineer
IBM Power Systems
IBM Suisse
Rue Eugène Marziano 25
1227 Les Acacias
Jean-Manuel Lenez
jlen@ch.ibm.com

## Slide 2
AGENDA
- AIX & System software
- Power Enterprise 2.0
- Entitled Systems Support (ESS)
- HMC / vHMC
- IBM Cloud : Power Virtual Servers
3. Futures annonces
1. Software
2. Infrastructure

## Slide 6: & Systems Software

## Slide 7: AIX Support Matrix
New Innovation are put in our most current release stream which is AIX 7.2
The last AIX 7.1 TL shipped 4Q2017
AIX 6.1 is in its extended support period (confirmed until April 2020)
AIX 5.3 will finally have its end of life in April 2019
  no possibility to run AIX 5.3 supported beyond that date
  no security fixes will be provided any longer
2019 is end of service for POWER5, POWER6, and POWER7 !
Power Platform | AIX 5.3 | AIX 6.1 | AIX 7.1 | AIX 7.2
POWER4 |  |  |  | 
POWER5 |  |  |  | 
POWER6 |  |  |  | 
POWER7 |  |  |  | 
POWER8 |  |  |  | 
POWER9 |  |  |  | 
Not Supported
Supported in
Native Mode
Support expired
Supported in
P6 Mode
Supported in
P7 Mode
Supported in
P8 Mode
Notes: This charts captures the AIX support matrix and which AIX release stream is supported on which Power generation
It has details on our release strategy as well.

## Slide 8: AIX 7.2 Enhancements
New Levels of Workload Scalability
  SMT 8 default mode for P9
  1536 threads in a single LPAR
  32 TB RAM in a single LPAR
  DSO support for P9
New Levels of OS Security
  AIX Secure Boot
  Trusted Install and Update
  Option to restrict AIX kernel trace to only privileged users
Enhanced Automation & Ressource Management for AIX Live Update
  LPM automation to manage live update operations that require available resources on a different server
  Enhanced CPU management to reduce overall frame required CPU for a live update operation
New I/O features
  PCIe U.2 NVMe SSD
  PCIe4 2-port 100Gb RoCE EN100Gb adapter
MPIO Enhancements
  MPIO enhancements to support disk storage attached through the AIX iSCSI software initiator
  Enhancements for MPIO storage resiliency
JFS2 file space reclaim
  JFS2 file space reclaim for enhanced efficiency with thin provisioned storage solutions
  Enhanced support for alt_disk_mksysb installs
  allows customized boot images to be copied during alternate disk maintenance
AIX Toolbox Updates
  New open source tools and solutions for AIX available from the AIX Toolbox for Linux applications, like R, PostgreSQL, clamav and Mongoc
  Faster mobility and improved security & compliance by
coupling compression and encryption of LPM data
RFA: https://www-01.ibm.com/common/ssi/cgi-bin/ssialias?htmlfid=897/ENUS218-381&infotype=AN&subtype=CA

## Slide 9: AIX Live Update Evolution
AIX 7.2 TL0: Introduction of AIX Live Update
  Apply an i-fix without having to reboot
AIX 7.2 TL1: Live update for any Update
  i-fixes
  PTFs
  SPs
  TLs
AIX 7.2 TL2: Simplification / Extended Scope
  Live Update support for PowerVC
  Live Update Integration with Power Enterprise Pools
AIX 7.2 TL3: Simplification / Extended Scope
  Live Update Integration with LPM
  Live Update CPU Reduction
Notes: Dave

## Slide 10: Non-Volatile Memory express - NVMe
NVM Express (NVMe) or Non-Volatile Memory Host Controller Interface Specification (NVMHCI) is a logical device interface specification for accessing non-volatile storage media attached via a PCI Express (PCIe) bus
P9 scale-out systems will support up to 4 400GB M.2 form factor NVMe devices The 2 internal direct attached storage connectors on P9 scale-out systems can support
  a SAS controller requiring DASD backplane or
  NVMe carrier cards to which up to 2 400 GB M.2 form factor mainstream NVMe drives can be attached
  M.2 NVMe on P9 SCO do not support concurrent maintenance
P9 scale-up systems will support up to 4 U.2 2.5” 7mm form factor NVMe devices
  4 hot plug capable U.2 drive bays exist on the CEC
Notes: So, Nvme is a device interface spec for accessing non-volatile storage via PCIe and has been designed to allow host HW and SW to fully exploit teh levels of parallelism possible with modern SSDs.
As a result it reduces I/O overhead and brings various perf impr.
In comparison to previous device interfaces, including multile, long command queues and reduced latency

## Slide 11: AIX NVMe-oF
NVMe over Fabrics (NVMe-oF) consists of many evolving and competing technologies
Major storage vendors are offering some form of NVMe-oF attach
  Extends existing internal NVMe storage to external/sharable NVMe-oF storage
NVMe over Fibre Channel (FC), also called FC-NVMe
  Allows one to use existing SAN infrastructure with updates on the storage and host side: Gen 6 FC switches can support FC-NVMe
  Same host side FC port can be used simultaneously for both FCP (FC SCSI) and FC-NVMe
  Same target side FC port can also be used simultaneously for both FCP and FC-NVMe
AIX NVMe over Fibre Channel (FC)
2019
  Only available on existing 32 Gb FC adapters
  Support for MPIO FC-NVMe
  Initial support IBM storage (FS 9100 etc). Expand storage portfolio over time.
NVMe over FC boot support added in 2020
Virtualization at a later date
All statements regarding IBM's future direction and intent are subject to change or withdrawal without notice, and represent goals and objectives only

## Slide 12: AIX Release Roadmap View
2016
2017
2018
2019
2020
2021
2022
2023
2024
AIX 6.1 GA 11/2007
EOL
EOM 4/16 EOS 4/17
AIX 7.2
GA 12/2015
Fee-based service extension
Marketed and serviced
Serviced only
AIX 7.1 GA 09/2010
EOL
EOM
TL5
TL1
TL2
AIX Next
Future
???
EOS
2025
2026
2027
2028
Technology Level (TL)
Last TL
P9 Enablement SPs
TL3
All statements regarding IBM's future direction and intent are subject to change or withdrawal without notice, and represent goals and objectives only.
Notes: 12
Long term commitment
we will continue investing in AIX to deliver technical innovations and modernizations along with continue to maximize performance, reliability, and security.
AIXnext!?The topic around new OS release numbers pops-up quite a bit when talking to clients, business partners and even internals, these days…
The reason why we did not introduce a new major release like ‘AIX 8’ yet is because we are able to introduce all new features via TL's - so there is no need for a massive kernel change that would force a new release number, which will force ISVs to re-compile, re-test and re-certify their SW …
So bottom line is that the lack of an AIX higher release number is a major strength and not a lack of strategy, roadmap or future investment plans.
- And the only reason to do that would be to satisfy analysts or marketing…

## Slide 13
Versions IBM i et TR (Technology Refresh)
2010
7.1
7.2
2014
…
IBM i next + 1
2016
IBM i next + 2
7.3
7.3 TR6
2019
Disponible depuis le 10.05.2019
Arrêt de support depuis le 30.04.2018
7.4
Arrêt des évolutions depuis le 30.04.2019
Disponible le 21.06.2019

## Slide 14
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
VIOS Releases & Lifecycle
Marketed and serviced
Fee-based service extension
ifix’s only, no new HW enablement
Technology Level (TL)
Service Pack
  A VIOS 3.1.0, 2.2.6, and 2.2.5 supported on are POWER9
  VIOS 3.1 and VIOS 2.2.6 images available on IBM ESS (Entitled Software Support) website
VIOS 2.2.4
GA 12/15
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
VIOS 2.2.6
GA Oct 2017
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
Optional Extended Support available, Special Bid Process.
iFIX support for bug fixes only, does not include enablement of new HW
SP
End of standard support
VIOS 2.2.5
GA 4Q/16
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
VIOS 3.1.0
GA: Nov 2018
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
AIX 7.2 Based
AIX 6.1 Based
AIX 6.1 Based
AIX 6.1 Based
VIOS 3.1.1
ETA: Nov 2019
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
AIX 7.2 Based
All statements regarding IBM's future direction and intent are subject to change or withdrawal without notice, and represent goals and objectives only

## Slide 16
New Back-up to the Cloud Option
New Metrics that allow to track failover times and calculate recovery time
Automated offline backup (SVC only)
Policy-based incremental and full backups
Support for one-site and multisite deployments
Every POWER9 based server workload is virtualized, mobile and fully cloud-enabled with PowerVM
Live migration from POWER7, POWER8 to POWER9 based systems with Live Partition Mobility
Mobile workloads are compressed and encrypted for improved security and acceleration
Simplify Management of Security & Compliance across AIX and LoP
Improved real-time Malware detection
Enhanced compliance automation with support for GDPR
Scalability enhancements incl. REST APIs
Improved Audit support (end-to-end) incl. a new interactive time-line
VMR HA / VMR DR
Export / Import capability to share images across data centers /clouds
Integration with Spectrum Scale to support SAN-less Clouds
OpenPower Support: Seamlessly manage AIX, IBM i and cloud native appl. with a single pane of glass
Support for IBM Cloud Private
MFA
Enhanced support covering AIX, Linux on Power, and the HMC
Additional factors in addition to RSA SecurID and certificate based smart cards were added - such as TOTP on your phone, Yubikey, Radius protocol, and more
VMR provides a simplified VM replication and restart solution
Server, VM, and workload-level HA OS agnostic
Co-location and anti-colo policy support
Non-disruptive DR rehearsal
Application monitoring agents for DB2, Oracle, and SAP HANA
Power Systems Software Highlights
Notes: Our various Power Systems SW offerings are gaining momentum and were enhanced broadly with capabilities – most of which focus around cloud.
So this is a one pager summarizing the most important improvements throughout our Power Systems SW portfolio

## Slide 17: AIX Purchasing Options / Considerations
AIX Std. Ed. continues to be marketed as is
perpetual and in form of AIX Monthly options
AIX EE continues to be marketed as is for now
set of bundled products won’t be changed
AIX Cloud Edition (Enterprise Cloud Edition with AIX)
A 3rd option how to purchase which might supersede AIX EE at some point in time
All orderable on any (P8/P9*) PowerVM based server!
* Cloud Edition is only avail. on POWER8 & POWER9

## Slide 18
Deploy & manage private clouds with simplicity
PowerVC Cloud
Spectrum Scale
Cloud Management Console
PowerVC Cloud
Self service infrastructure provisioning
Software defined solution for SAN less cloud
Single pane monitoring of all Power Systems infrastructure
AIX Enterprise Edition
Power Systems Enterprise Cloud Edition
PowerSC Std. Ed.
Simplify managing Security & Compliance
Big Fix Lifecycle
PowerSC MFA
PowerSC Std. Ed.
Security and Compliance management of cloud environments
Big Fix Lifecycle
Discover, secure and manage endpoints on different OSs
Raise the assurance levels with multi-factor authentication
Simplified high availability
VM Recovery Manager HA
Simplified HA solution for cloud deployments
Aspera
Accelerated file transfer in cloud environments
High Speed file exchange between private and public clouds
Cloud App Management
Application aware infrastructure monitoring and analysis
ITM6
AIX Std. Ed.
AIX 7.2 Std. Ed.
OS
with AIX
Rapidly deploy Power Cloud Infrastructures with cost-effective Software Bundles
pids: 5765-ECB
5765-CBA
Notes: 1. This slide shows what clients will get out of this bundled components capability and value wise…
<walk through>
2. As mentioned, this bundle could be deployed on top of any of our OSes running on Power, but at this time primarily benefits AIX & LoP, as several components do not (yet) support IBM i.
3. But as mentioned, this bundle actually comes in 2 flavors and the 2nd one incl. AIX 7.2 Std. Ed. Which allows for smooth upgrades for clients coming from AIX EE that might be interested in upgrading to this bundle.
4. And as you can see, there were quite a few offerings / capabilities added compared to AIX EE
For the time being, AIX EE will be continued to be marketed as is. But this new cloud edition is intended to be its successor in the mid or longer-term.
Let me pause here and see if we have any questions before talking about these components and capabilities in detail…

## Slide 19: Smooth Migration to P9 from POWER7 & POWER8
Live Mobility Considerations (P9 Compatible Mode Architecture)
VMs running AIX levels supporting P9 can be live migrated from P7 or P8 to P9 systems and be run there as is – without workload interruption!
  VMs running on P6 or below must first be migrated to P7 / P8 systems and rebooted before being migrated to P9 systems
Delivering mobility on every PowerVM server makes migration the obvious choice
PowerVM (Enterprise Edition) included with all models
  LPM capability can be deactivated (f. Oracle audits etc.)
PowerVM Linux Edition remains optional for L models
PowerVM remains unavailable for LC models
 No change to PowerVM on Power8
  Added by default to server orders in eConfig (deselectable)
  WFM/EOL for PowerVM Standard Edition aligns with final WFM of Power8 models
LPM can be used to quickly and easily move workloads from P7 / P8 to P9 systems!
a free 60-day activation can be requested (Feature Code ELPM)
Notes: VM EE in any VM based server
And we made it really easy for clients to move to P9, as every P9 PowerVM based server is cloud enabled (as it incl. LPM)
For clients that are just running PowerVM Std. Ed. There is a free 60-day activation feature avail. That they could leverage to use LPM to move to Power9 without disruption.
So key Message on this chart and I think a good value proposition: you can take your system as is – running today and migrate, without interruption
- So you can take AIX workloads running on P7 & P8 and migrate via LPM without having to recompile or change workloads or even stop workloads
(Basically if using any AIX level released in the last 24 months – which is basically all under the 2nd bullet on the previous chart, you can leverage live LPAR Mobility)
-> LPARs running P6 must first migrated to P7 or P8and rebooted before being migrated
-> and if you would like to run in P9 mode so to speak to leverage new features, you need to reboots LPARs running AIX 7.2 TL2 first

## Slide 20: LPM Compression & Encryption in P9 (Scale-up)
Adding LPM encryption in FW920 – the P9 advantages
  Using the on chip accelerators
  Coupling compression & encryption together providing huge performance improvements
Up To 5x Reduction in LPM time
To be introduced on Power9 scale-out as well!
Notes: In 3rd quarter in conjunction with the scale-up boxes launch, we introduced the capability to compress and encrypt LPM data,
which helps speeding up live partition mobility operations tremendously, but as well makes them more secure as data in flight is protected.
-> this gives us a very good story compared to what vmware provides – as they only use SW encryption while we doing that on-chip – which gives us an enormous performance advantage

## Slide 21
Entitled Systems Support (ESS)

## Slide 22: Capacity on Demand (COD) Offerings
COD Type | Description | Power FW Levels
Permanent | Static permanent license on this server only | 7 / 7+ / 8 / 9
Trial | One-time free enablement of anything unlicensed, for 30 days, to study benefits of additional resources | 7 / 7+ / 8 / 9
Legacy Elastic COD | Temporary daily access to resources, billing based on access metrics reported back to IBM and usage on server ordered against. Post pay with enablement key via e-config MES order or through the Web: ECOD website Pre-paid with billing features via e-config MES order | 7 / 7+ / 8 / 9
NEW Elastic COD | Temporary daily access to resources, using pre-paid infrastructure with many advantages including usage across multiple servers Customer direct pre-paid orders through Markeplace/ESS BP/Sales pre-paid orders for customer through new Virtual Capacity1 billing features via e-config initial/MES path orders Customer provision and generate ECOD usage across any P8 or P9 systems in their enterprise | 8.4, 8.6 / 9
Utility | Processors assigned to shared processor pools. Usage accrues only when processing demands exceed non-Utility processors. Billing based on reported usage. | 7 / 7+ / 8 / 9
Enterprise Pools | Group of servers, entitlement for dynamic movement and resource usage on any server in pool. Entitlement fully purchased once, no future billing. | 7+ / 8 / 9
1. Ordering Elastic Capacity days in e-config/Partner Commerce for automatic provisioning through Marketplace/ESS is projected to be available early 4Q 2018 .
Notes: This is a view of all our Power Capacity on Demand offerings. While you may be familiar with these I wanted to briefly cover them to show the level of flexibility we have to enable our clients in tapping into the on demand processor and memory resources that comes with their Power Enterprise servers.
There is Permanent Capacity on Demand which is the static processor and memory resources you purchase with your server
Trial Capacity on Demand which upon request and approval provides a one time limited access to processor and memory resources for 30-days trial
Utility Capacity on Demand which gives access to processor only resources assigned to a share processor pool for automatic by the minute usage when demand exceeds your non-utility processors.
And Enterprise Pools which allows you to share mobile processor and memory resources across a pool of servers with Power 8 and Power 9 High End servers in a pool
In addition there is the Legacy Elastic Capacity on Demand which provides temporary daily access to additional processor or memory resources but through our legacy process of acquiring enablement key and billing through monthly usage reporting to IBM and MES order of billing features to cover your usage. This legacy Elastic COD can only be used on the server it was enabled and purchased for and requires signing of contracts and IBM seller or BP setup that takes weeks.
Finally our new Elastic Capacity on Demand through the web that provides the same daily access to untapped processor and memory resources but with unparalleled flexibility and self service capabilities to the client. Clients can order and provision directly on the web in minutes, they can order through their IBM Seller or Business Partner and they can provision and use the resources across any P8 or P9 system in their enterprise.

## Slide 23: Power Enterprise Pools and Elastic Capacity can help enable a seamless transition to POWER9
Master HMC
Automation of Mobility with
Power Enterprise Pool
Elastic Capacity from
IBM Marketplace/ESS1
Power E850C
Interoperability between POWER8 & POWER9 (SOD*)
Elastic, On Premises cloud consumption model with IBM Marketplace/Entitled Systems Support (ESS) for POWER8 and POWER9
POWER950
POWER980
Managing
HMC
Managing
HMC
Power E880C
Power E870C
Notes: 23
23
23
With our new Power E950 and E980 enterprise or scale up servers, Power Enterpise Pools and Elastic Capacity on demand enables a seamless transition to Power9 and deliver on-premise cloud like consumption capabilities that allows full capex to full opex consumption models with the experience of public cloud and benefits of a private cloud environment.
Elastic Capacity on demand through the Entitled System Support (ESS) website or mobile app can now, either be purchased on the web by your client or purchased by an IBM seller or Business Partner through PC (Partner Commerce), WTAAS, or iEPR on an e-config configuration. The Elastic Capacity on demand days purchased can be provisioned in minutes across multiple servers on the entitled systems support (ESS) website or mobile app. As with Power Enterprise Pools, This new Elastic Capacity on Demand can be used across both power8 and power 9 systems and days purchased for an E980 for example can be used across any E980, E880, E880C, E870C or E870 in your enterprise.
This is the way that we hope to deliver capacity on-demand infrastructure with a the flexible, self-service model to our clients moving forward!

## Slide 24: How it works
From purchase to active capacity on systems in less than 5 minutes directly or through the IBM Seller/Business Partner in 1-2 days
Purchase Elastic Capacity through Marketplace/Entitled Systems Support (ESS) or order through IBM Seller or Business Partner
Unlimited amount of processor cores or memory can be purchased in a single transaction
Download keys for activations for systems anywhere in client’s enterprise
System notifies end user when running low on purchased ECOD days
Purchase through Marketplace/ESS or e-config/Partner Commerce
1
2
Activate on any system / Download in minutes
3
Client invoiced based on aggregated orders
Notes: Next I will go through a bit more details on how Elastic COD works for the client and IBM Seller or Business Partners.
Clients can go from purchasing to activating capacity on their systems in less than 5 minutes. Partner can purchase capacity and have it automatically available to the client for provisioning and usage in 1-2 days with no back and forth contracts, monthly reporting, and acquisition of enablement keys.
Again.. Unlimited amount of processor cores or memory can be purchased in a single transaction and keys/codes for activation can be generated for systems anywhere in clients enterprise across the same country. The system also notifies the end user when they are running low on ECOD days so they can order before resources are depleted. If a client goes over their allocated resources the system will deduct the overage from any new key generated for that system.

## Slide 25
Power Enterprise 2.0

## Slide 26
1999
Logical Partitions
2001
Dynamic LPARs
2002
Capacity Upgrade on Demand
2007
Utility CoD
Live Partition Mobility
Virtual I/O
Proven record of virtualization innovation
2004
Micro-partitioning
2019
Power Enterprise Pools 2.0
2012
System Pools
Power Flex
2010
2013
Power Enterprise Pool
2017
Elastic COD via ESS
Notes: Power Systems has a rich history of virtualization innovation and delivering seamless growth, non-disruptive growth and flexible capacity to our clients. It stems from the deep integration of PowerVM virtualization with Power Server hardware.
Clients have leveraged the ability to utilize their processors and memory more flexibly within a system since Logical Partitions were introduced in 1999, approximately 20 years ago. The ability to dynamically adjust processor and memory capacity between partitions has been available almost as long, and micro-paritioning enabled even more granular use of system resources to deliver more ROI to IT teams to be responsive to changing capacity requirements within a system.
On/Off Capacity on Demand delivered temporary capacity to clients for processor & memory by the day. Utility on Demand offered automated, dynamic processor by-the-minute capacity for short term spikes.
As Power servers became massively scalable, IBM increased the options for clients to get even more ROI from their IT investment by enabling resource sharing of CoD resources between systems within an enterprise, with Power Flex on the Power 795 and with Mobile Processor & Memory Activations on POWER7+ and POWER8. Elastic COD was made simpler with self-service provisioning of keys to offer clients the ability to provision purchased eCOD capacity across their systems themselves.
Delivering multi-system flexibility with Mobile resources within a Power Enterprise Pool has proven invaluable to clients with high-end Power systems as the foundation of their mission-critical business infrastructure.
As part of a multi-year collaboration with key clients, IBM is announcing new levels of resource sharing within an enterprise with Power Enterprise Pools 2.0. We believe Pools 2.0 will combine the best attributes of Elastic Capacity on Demand, Utility on Demand and Power Enterprise Pools to provide more ROI and simplify the ability to capitalize on resource sharing with fully-active servers that provide consumption-based IT options for optimizing TCO in an on-premises private cloud infrastructure.

## Slide 27
Base and Metered Capacity
Processor activations
Memory activations
AIX and IBM i licenses
Usage tracked by the minute via IBM Cloud Management Console
Power Enterprise Pools 2.0
All processor & memory resources are fully activated
Automated capacity management
Shared Utility Capacity across a pool of Power E980 systems
Purchase System and Base capacity
Variable demand addressed by purchasing Capacity Credits for Metered capacity
Cloud Management Console with HMC automatically tracks and debits against Capacity Credits based on actual usage
RFA: https://www-01.ibm.com/common/ssi/ShowDoc.wss?docURL=/common/ssi/rep_ca/3/872/ENUSAG19-0003/index.html&lang=en&request_locale=en
UBS Lab Day 2019 / AIX Trends & Directions / May, 2019 / © 2019 IBM Corporation
Notes: EP 2.0 in CMC:
Inventory
Displaying, Monitoring & Managing a Pool
Advanced Monitoring
Analyze Total or Metered Usage
Usage by resource type
Metered Usage Statement
Show Capacity Credits consumed and breakdown by resource

## Slide 28
32
32
32
32
32
32
32 Base
128 Installed
64 Base
128 Installed
96 Base
128 Installed
Pool = 192 Base
Pool = 384 Installed
192
192
32
96
64
Client purchases Power E980 systems with permanent, active resources (Base) and inactive, “dark” resources that may be activated temporarily (Metered)

## Slide 29
32
32
32
32
32
32 Base
128 Installed
64 Base
128 Installed
96 Base
128 Installed
Pool = 192 Base
Pool = 384 Installed
192
32
192
32
32
32
32
32
32
Everything activated, processor, memory & license entitlement monitored by the minute
Resource usage metered for minutes above the pool’s aggregate Base resources
Base
Base
Base
Base
=
Power Enterprise Pool 2.0

## Slide 30
32
32
32
32
32
32 Base
128 Installed
64 Base
128 Installed
96 Base
128 Installed
192
32
192
32
32
32
32
32
32
Pool
0 Metered
192 Base
384 Installed
192 aggregate for pool
64 used
32 used
96 used
=
Usage Example - Pool has 1 system using more than its Base Processor Activations, but another system is using less than its Base Processor resources, so 0 Metered Usage recorded

## Slide 31
32
32
32
32
32 Base
128 Installed
64 Base
128 Installed
96 Base
128 Installed
Pool
32 Metered
192 Base
384 Installed
160
32
192
32
32
32
32
32
32
32
224 aggregate for pool
64 used
64 used
96 used
=
32
Usage Example - Pool measures > the aggregate of Base Processor Activations across the pool, so 32 Metered Processor Capacity minutes are recorded and Metered Capacity Credits are debited

## Slide 32
HMC / vHMC

## Slide 33: Release Roadmap
HMC/vHMC
IVM
HMC V9 / POWER9
IVM service stream
CMC
3Q / 18
1Q / 18
HMC 9.1.910
vHMC
x86 &
ppc64le
HMC 9.1.920
vHMC
x86 &
ppc64le
Continuous Delivery
2Q / 19
HMC 9.1.930
vHMC
x86 &
ppc64le
HMC 9.1.940
vHMC
x86 &
ppc64le
4Q / 19

## Slide 34: Hardware Roadmap
x86
HMC V8
HMC V9 / P9
3Q / 17
Power
HMC 8.7.0
3Q / 18
1Q / 18
HMC 9.1.910
HMC 9.1.920
CR5, CR6, C08
unsupported
7063-CR1
CR9
EOM*
2Q / 19
HMC 9.1.930
*See https://www-01.ibm.com/common/ssi/ShowDoc.wss?docURL=/common/ssi/rep_ca/5/877/ENUSZG18-0045/index.html&request_locale=en
for info regarding 7042 withdrawal.

## Slide 35: x86 HMC Withdrawal
HMC V9 / P9
3Q / 18
1Q / 18
2020
ppc64 – 7063 hardware appliance &
vHMC on x86 & ppc64le
HMC 1.910
managing
server A with 910 firmware
HMC 1.920
managing
server A with 910 firmware
server B with 920 firmware
HMC 2.950
managing
server A with 930 firmware
server B with 950 firmware
server C with 950 firmware
x86 – 7042 hardware appliance
HMC 1.910
managing
server A with 910 firmware
HMC 1.920
managing
server A with 910 firmware
server B with 920 firmware
HMC 1.940
managing
server A with 930 firmware
server B with 950 firmware
server C with 950 firmware
Fix support for existing in-support releases for the x86-based HMC appliance will remain unchanged. See http://www-304.ibm.com/support/customercare/sas/f/power5cm/supportedcodeHMCHW.html for the lifecycle of releases.

## Slide 36: HMC Version Format – Version 8
Not currently used
aka Service Pack
  ex. SP1
Corresponding firmware release
  ex. 860
Must be greater than or equal to the level this HMC is managing
Power family
  ex. POWER8
M(aintenance)
R(elease)
V(ersion)
F(ix)
A release is supported for two years
  This includes Service Packs and PTFs
  There are four to five releases in support concurrently at any given point in time.
Many clients have strict processes and procedures in place that prevent upgrading to a new release in cadence with when IBM GAs it.
  It's not always possible to obtain the latest functional fixes and enhancements as they're typically issued on the latest release stream.
From the perspective of security alone in how often, and with what severity, vulnerabilities are disclosed, the above two points are proving to be more and more of an issue.

## Slide 37: HMC Version Format – Version 9
aka PTF
lshmc output will show “MH” mapping
Corresponding firmware release
  ex. 910
Must be greater than or equal to the level this HMC is managing
Last digit indicates Service Pack
Only increment on major revisions
  ex. base OS upgrade
  much less frequency than today
Power family
  ex. POWER9
M(aintenance)
R(elease)
V(ersion)
F(ix)
A release is supported for two years, same as today.
Maintenance releases will be supported until they're superseded by the next subsequent maintenance level
The cadence with new firmware releases and Power system models will remain unchanged.
  Rather than receiving a new HMC release, (more often than not) there will be a new HMC maintenance level.
  When there's no new firmware or Power system model, there can still be a new HMC maintenance level.
Less releases allow freedom to update to the latest maintenance level without worrying about stack (VIOS, firmware, OS) compliance.
Easier to stay current with functional fixes and enhancements. IBM can focus mostly on the current release (because there will be less releases) and making sure each maintenance level is delivered with increased quality.

## Slide 38
IBM Cloud : Power Virtual Servers
https://www.ibm.com/cloud/power-virtual-server

## Slide 39: IBM Power Virtual Server for IBM Cloud
Offering Description
Clients and business partners can self-provision and purchase monthly subscription Power IaaS cloud instances from IBM Cloud.
Clients get self-service VM lifecycle management within a pool of compute, memory, storage, and network infrastructure. Clients access Power VMs through client owned IBM Cloud resources.
IBM manages and supports up to OS deployment and the client self-manages the OS and up. Clients can bring their own OS images or add to available OS images.
Multi-tenant, self managed, Power compute as-a-service in IBM Cloud with consumption-based OPEX pricing
Partner Value
IBM Value
Notes: IBM Power Systems for IBM Cloud is a Power infrastructure as a Service (IaaS) offering available from the IBM Cloud catalog. The offering delivers POWER9 based server technology providing IBM AIX and IBM i choices for clients to create cloud environments for their mission-critical workloads without changing their core platforms.
Clients and business partners can self-provision and purchase monthly subscription of Power cloud instances from IBM Cloud.
Clients get self-service VM lifecycle management with a pool of compute, memory, storage, and network infrastructure.
Clients access Power VMs through client owned IBM Cloud account.
IBM manages and supports up to OS deployment and the client self-manages the OS and up. Clients can bring their own OS images or select one of the pre-defined OS images available. .
General availability (Limited) for AIX and IBMi is June 15, 2019 and will offer Availability Zones (AZs) in Dallas and Washington, DC. The support will later expand to other AZs in Europe, Canada, and other global locations based on customer demands.
Let’s look at the solution concept highlighted on the right hand side of the chart. IBM Power Systems deploy POWER9 systems , IBM storage and network through a POD that delivers adjacent services via IBM Cloud Service End-points.
Customers essentially purchases configureable Power Virtual Server capacity (e.g. compute capacity) and then self-provision multiple AIX instances and customize CPU core-count, Memory, and Networking based on their workload needs. The right to use OS license is included in the offering. However, customers can bring their own customized OS images for their workloads. Many Power clients already use IBM PowerVC to manage their virtual machine infrastructure in a private cloud. In this offering, we've developed a “VM Manager” that runs on IBM Cloud and integrates with the PowerVC API which then automates configuration of the Power infrastructure. The UI for this powerful management layer can be accessed via Web and Command-line interfaces.

## Slide 40
S922 or E880
0.25-143 cores (15 for S922, 143 for E880/980), Dedicated or Shared option
8-64 GB per core
Type: Tier 3 (HDD) or Tier 1 (SSD)
10 GB minimum / 2 TB maximum per disk, 10 GB increments
Public and/or Private IP
AIX 7.1 / IBM i 7R2 7R3
Offering Name:
IBM Power Systems Virtual Server on IBM Cloud
IBM Offering
Offering Description:
A user can purchase an AIX or IBM i Power VM-based Virtual Machine-as-a-Service on IBM Cloud. IBM manages up to OS deployment and the client self-manages the OS and up. Our users can purchase the offering through Cloud consumption-based pricing plans available through IBM Cloud Catalog.
MVP Offering:
Systems:
Compute:
Memory:
Storage Type:
Storage Quantity
Network:
OS:

## Slide 42
Beta features:
•Create VM with independent control over cpu, ram, data volumes, and the source VM Image
•Provide SSH keys for a VM - no Key Protect integration
•Delete VM
•Modify VM (cpu & mem DLPAR)
•Stop VM
•Start VM
•Create Data Volume
•Open console to a VM
•List VMs
•Show cloud instance resources (cpu, ram, disk, etc.)
•Bring Your Own Image
•Full function GUI, CLI, and REST API
GA features**
•Assign VM label or tag attributes
•Modify LUN (Grow)
•VM Location Policies for affinity
•Capture VM
•Export VM Image
•Import & export Data Volume
•Metering & billing
•Performance statistics (cpu, mem, i/o, etc.)
** new features will be delivered in an iterative model as they are developed.

## Slide 43
Q2 ‘19
Availability
(June 15) Select Availability (US East / South)
Specifications
E880 and S922 LPARS (PowerVM based) w/ IBM storewide v7000 storage (SSD and Disk)
US East and South (Dallas) availability
US East availability (Washington DC)
IBM Cloud / DOC ID / Month XX, 2018 / © 2018 IBM Corporation
Q3 ‘19
(May) Beta in WDC
Offering Roadmap
September Frankfurt availability (Multi Datacenter HA)
Post-GA Geo Expansion
Consequent rapid expansion into other Geos (UK, TOR, AP and beyond)
Geo Expansion
Q4 ’19 - 1H2020
Terraform Provider
Post-GA Functionality
E980 available in FRA
HIPPA Readiness
Post-GA Compliance
Integrated DRaaS
Future Functionality
Backup as a service
Linux on PowerVM
SOC2
Future Compliance
ISO 27001

## Slide 44: Workload Positioning: IBM Power Virtual Server for IBM Cloud
Sales & GTM
 | Test/Dev | Resource scaling in Cloud | Hybrid Multicloud
Use Case Description | Provides a way to carve out a sandbox for test and development for deployment in production later. Precious resources remain on-premise. | Centralized IT remains on-premise to deliver applications and services for Organization but when required, can take advantage of public-cloud based resources to deliver peak Operational performance plus Opex/CapEX saving. | Leveraging Cloud Native services and architectural patterns to transform business models through Modernization.
Business Drivers1,2,3 | Easily scale/Faster time to market | Pay for what is consumed | Application Modernization
Notes: Target Audience: IBM Sellers and Business Partners
Usage Guidance: This chart is intended to be used in conjunction with additional Offering specific charts which provide more detailed specifications along with some Architectural patters based on each use-case.
Speaker Notes:
  To Support existing IBM Clients that are using IBM’s AIX and IBM i operating systems for their Business and/or Mission Critical applications, we have announced IBM Power Systems Virtual Server on IBM Cloud. This Infrastructure as-a-Service (IaaS) offering delivers a simple and Self-service method for clients to make the next journey of their digital transformation easy.
  In this environment, Clients can provision IBM Power9 Compute with Block Storage based on Spectrum Virtualize technology and networking that allows flexibility to deliver on numerous Use-Cases across industries. For starters, we have highlighted (4) simple Use-cases that enables Resiliency, Expansion without Construction, Pay/Go Consumption model, Application Mobility and more. These Use-Cases combined with Cloud Services allows customers to take existing workloads and scale them flexibly to fine-tune their business model no matter where they are in the Cloud Transformation journey. This Offering intends to leave no customer behind in the journey to Cloud adoption.
References:
  Five Business Drivers For Organizations Moving To The Cloud (Papolou, R. ) (Website: https://www.forbes.com/sites/forbestechcouncil/2018/05/22/five-business-drivers-for-organizations-moving-to-the-cloud/#20c3b8804558)
  What are the Business Drivers for Containers? Five Examples (Website: https://www.sdxcentral.com/containers/definitions/what-are-the-business-drivers-for-containers-five-examples/)
  Scaling Business Intelligence in the Cloud (Website: https://datometry.com/resources/case-studies/scaling-business-intelligence-cloud-case-study/)